## Slide 1
Deep Learning–Based Spectrum Sensing under Partial Observations
Submitted by:
Chetan Prakash Dudi Roll No: 2022CSB1074
Manish Anwla Roll No: 2022CSB1090
Under the guidance of:
Dr. Sudeepta Mishra & Anjani Gupta
Department of Computer Science and Engineering Indian Institute of Technology Ropar

## Slide 2
Motivation:
  Wireless spectrum is crowded, like a busy bazaar where everyone wants a stall.
  Primary Users (licensed) must be protected from interference.
  Secondary Users need reliable spectrum sensing, especially under low SNR and partial visibility.
1
Objective:
  Build deep learning models (LSTM, Bi-LSTM, GRU, RNN, Enhanced LSTM) to detect PU activity.
  Compare with state-of-the-art Collaborative CNN from IEEE TCCN 2024
2
Project Overview (Before Mid-Semester)

## Slide 3
Problem:
  Efficient spectrum sensing fails when
    SNR is very low
    Each SU sees only a slice of the spectrum (“partial observations”).
  Conventional methods (Energy Detection, Cyclostationary) crumble under noise uncertainty.
Problem Statement & Research Gap (Pre-Mid-Sem Work)
Research Gaps Identified:
  Partial Observations Issue:
  Existing DL models assume full-spectrum input → unrealistic.
  Temporal Dependencies Ignored:
  PU activity has patterns over time; CNNs can’t capture these well.
  Model Complexity vs Robustness:
  Collaborative CNNs reduce parameters but still need coordination.
Our Direction:
  Explore LSTM-based models to capture long-term temporal behaviour.

## Slide 4
Data Pipeline Built:
  Synthetic PSD dataset across SNR = −16, −10, −4 dB.
  PSD shape: 64 frequency bins × 20 bands per sample.
  Labels: Occupied / Idle for each of 20 bands.
Pre-Mid-Semester Work Summary
Preprocessing Completed:
  Standardization of PSD values.
  Sequence conversion: (20 time steps × 64 features).
  Train/test splitting & DataLoader setup.
Baseline Evaluation Done:
  Training convergence plots
  ROC curves
  PD vs SNR
Model Implementations (PyTorch):
  LSTM, Bi-LSTM, RNN, GRU, Enhanced Gated LSTM
  Loss: Binary Cross-Entropy
  Optimizer: Adam
Pre-Mid-Semester Work Summary

## Slide 5
An I/Q signal is a way to represent a complex signal using two real signals:
I → In-phase component
Q → Quadrature component (90° phase shifted version of I)
Post Mid-Semester Progress Overview
Purpose: Generate wideband wireless I/Q datasets using GNU Radio and SDR.
1
Goal: Capture real-world signals under varying channel conditions for IoT and modulation analysis.
2
Devices: ADALM-PLUTO SDR, GNU Radio, Python (PyTorch) integration.
3
Output: Dataset of PSD, SNR, and PU activity logs for each modulation type.
4
Mathematically, a complex baseband signal is written as:
x(t)=I(t)+jQ(t)
Where:
I(t) = amplitude of the cosine (real) part
Q(t) = amplitude of the sine (imaginary) part
j=sqrt(−1)​

## Slide 6
Software and Hardware Stack
Software:
  GNU Radio Companion
  Python (NumPy, Torch, CSV, FFT libraries)
  IIO Drivers for SDR communication
Hardware:
  ADALM-PLUTO SDR
  Frequency range: 325 MHz – 3.8 GHz
  Sample rate: Up to 1.024 MSPS
  NumPy: Used for fast mathematical operations like FFT and signal processing on complex I/Q data.
  Torch (PyTorch): Used to save and structure datasets (.pth files) for later ML-based signal analysis.
  CSV: Used to log real-time PSD, SNR, and PU activity values in a readable file format.
  FFT Library: Converts time-domain signals into frequency-domain (Power Spectral Density) for analysis.
  Frequency Range (325 MHz – 3.8 GHz): Defines the tunable radio spectrum that the PlutoSDR can operate in.
  Sample Rate (up to 61.44 MSPS): Determines how many signal samples are captured per second, affecting bandwidth and accuracy.

## Slide 7
Overall System Flow
Primary User (PU): Transmits modulated signal using GNU Radio and Adam Pluto SDR.
Secondary User (SU): Receives signal and logs spectral data.
Data Flow:
  Generate binary data by Matlab.
  Modulation applied (BPSK/QPSK/FSK/16QAM).
  Signal transmitted using PlutoSDR Sink.
  SU receives via PlutoSDR Source and runs Python logger.
PU block
Air
SU Block
Logger

## Slide 8
Overall System Flow

## Slide 9
Transmitter Flowgraph (PU_tx.grc)
Blocks Used:
  File Source → Constellation Modulator → QT Frequency Sink + PlutoSDR Sink
Key Parameters:
  LO Frequency: 2.4 GHz
  Sample Rate: 1.024 MHz
  Buffer Size: 32.768k
Function:
  Generates and transmits I/Q data using chosen modulation.

## Slide 10
Transmitter Flowgraph (PU_tx.grc)

## Slide 11
Receiver Flowgraph (SU_rx.grc)
Blocks Used:
  PlutoSDR Source → QT GUI Frequency Sink → File Sink → Custom PSD Logger
Key Parameters:
  LO Frequency: 2.4 GHz
  Sample Rate: 1.024 MHz
  RF Bandwidth: 20 MHz
Function:
  Captures PU signals and logs Power Spectral Density.

## Slide 12
Receiver Flowgraph (SU_rx.grc)
Custom Python Block (psd_logger)
  Reads complex input samples from SDR source.
  Computes Power Spectral Density (PSD) in dB.
  Calculates SNR using mean PSD and 10th percentile noise floor.
  Flags PU presence (if SNR > 5 dB).
Stores results in:
  CSV: human-readable log
  PTH: tensor dataset
  Binned PTH: organized by SNR range (for ML)

## Slide 13
Receiver Flowgraph (SU_rx.grc)

## Slide 14
What is Modulation?
Modulation is the process of varying one or more properties of a carrier signal (like amplitude, frequency, or phase) in accordance with a baseband digital signal (data) that you want to transmit.
In simple terms:
Modulation converts digital data (0s and 1s) into an analog waveform that can be transmitted efficiently over a wireless channel.
Why is Modulation Needed?
Without modulation:
  Digital signals can’t travel long distances efficiently.
  Bandwidth and interference would increase.
  Multiple users can’t share the same frequency spectrum.
Hence, modulation helps to:
  Transmit data over long distances (radio frequency range).
  Allow multiple users to coexist (via different frequency bands).
  Improve resistance to noise and interference.
  Optimize bandwidth usage depending on channel capacity.
Modulation

## Slide 15
Modulation Description Data Rate Robustness
  BPSK 1-bit per symbol Low High
  QPSK 2-bit phase shift Medium Medium
  8PSK Frequency-coded Medium High
  16-QAM Amplitude + Phase High Lower
Observation:
  Higher-order modulations (QAM) give more throughput but are more noise-sensitive.
Modulation Techniques Used

## Slide 16
Impacts Of Modulation
When you transmitted using GNU Radio:
  The PU (Primary User) modulated binary files using BPSK, QPSK, FSK, and 16-QAM.
  The SU (Secondary User) received the waveforms and calculated:
PSD → how energy is distributed across frequency
SNR → how clear the signal is over background noise
You then used this data to log and analyze modulation performance under different noise and distance conditions.
So modulation directly impacted:
  The shape of the PSD you captured
  The SNR values stored in your CSV
  The PU detection accuracy (higher-order modulations harder to detect at low SNR)

## Slide 17
  CSV Columns: Timestamp | Mean_PSD_dB | SNR_dB | PU_Present
  PTH (Torch file) contains:
  PSD arrays
  Corresponding SNR values
  PU activity labels
  Used for wireless signal classification & IoT traffic pattern analysis.
Dataset & Logging Outputs

## Slide 18
Simulating Single PU-SU to Multiple PUs and SUs
Input Data
1
System Configuration
2
Concepts Used:
  Channel Gain
  Shadowing
  Frequency Drift
  AWGN
3
Algorithm
4

## Slide 19
Input Data (Real PSD Library):
  PSDs collected from real SDR hardware (Pluto/RTL-SDR)
  Stored inside .pth files per modulation:
  BPSK
  QPSK
  8PSK
  16QAM
  Each PSD: 192 frequency bins
  May include recorded SNR values
  Loaded into PSD_LIB for sampling
System Configuration:
  PUs = 10
  SUs = 10
  Channels = 20
  Freq bins per channel = 64
  One PSD (192 bins) split into:
  0–63 → Left leakage
  64–127 → Main signal
  128–191 → Right leakage
  Class count = 210=10242^{10} = 1024210=1024
Simulating Single PU-SU to Multiple PUs and SUs

## Slide 20
Simulating Single PU-SU to Multiple PUs and SUs

## Slide 21
Why do we use frequency drift?
Real radio signals do NOT stay perfectly centered at their exact carrier frequency because of:
  Local oscillator (LO) mismatch
  PLL instability
  Doppler shift (motion)
  Temperature changes
  Imperfect filters
  Hardware imperfections
Therefore, the received PSD will be slightly shifted left or right.
Important Terms(Concepts Used)
  Frequency Drift
To simulate this real behavior, we apply a fractional shift to the PSD bins.
Formula:
  If PSD = x[n]x[n]x[n] of length N and
  drift = Δf (fractional shift in bins):
  xshifted[n]=x[n−Δf]x_{\text{shifted}}[n] = x[n - \Delta f]xshifted​[n]=x[n−Δf]

## Slide 22
Base formula:
base_gain=(β⋅(d⋅A)α)−1\text{base\_gain} = \left( \beta \cdot (d \cdot A)^{\alpha} \right)^{-1}base_gain=(β⋅(d⋅A)α)−1
Parameter:
  α (alpha): Rate at which signal decays with distance
  β (beta): Constant scaling factor based on environment
  DIST_AMP: AAmplify the distance
Important Terms(Concepts Used)
  Channel Gain(Path-loss Model):
Why do we use channel gain?
Signal strength reduces when traveling from PU → SU due to:
  Distance
  Obstructions
  Atmospheric absorption
  Multipath fading
To model this attenuation, we use a log-distance path-loss model.

## Slide 23
Why do we use AWGN?
Every radio receiver experiences thermal noise:
  ADC noise
  RF front-end noise
  Mixer noise
  Amplifier noise
  Environmental EM noise
To simulate this, AWGN is added.
But the amount of noise must match the desired SNR.
Pnoise​=Psignal/SNRlinear​​
Important Terms(Concepts Used)
  Shadowing:
Why do we use shadowing?
Even at the same distance, signal power fluctuates due to:
  Buildings
  Trees
  Cars
  Humans
  Temporary blockages
This causes slow variations around the average path-loss.
This is called log-normal shadow fading.
  Additive White Gaussian Noise (AWGN):

## Slide 24
Algorithm

## Slide 25
Conclusion
  Implemented PU–SU communication using SDRs.
  Logged spectral features and generated datasets.
  Built foundation for AI-based modulation detection.

## Slide 26
A
Radio GNU Download Link
C
Results
PU_tx.grc
E
B
Pluto SDR Driver Link
D
SU_rx.grc
PSD logger Block Code
F
Resource
Page
GitHub Repo
G

## Slide 27
Thank you!